## Slide 1: Bubble Diagramming
Architectural Design – preliminary sketching
Copyright © Texas Education Agency, 2012. All rights reserved.
Notes: This presentation aligns with the lesson document, student handout, and the pop quiz.

## Slide 2: What is this?
Copyright © Texas Education Agency, 2012. All rights reserved.
ENTRY
LIVING ROOM
KITCHEN & DINING
MASTER BEDROOM
MASTER BATH
BATH
BEDROOM
BEDROOM
GARAGE
LAUNDRY
Closet
Closet
Closet
Notes: This is what a bubble diagram CAN look like. (Obviously, this one is drawn digitally so that it is easy to read for this presentation. On paper, when drawn by hand, they are much rougher). Now, begin demonstrating to students how to draw a bubble diagram. Talk them through it as you demonstrate. Bubbles represent spaces (such as rooms) in the house. Lines are connections between spaces, and do NOT necessarily mean that there is a hallway there! A line between bubbles can signal that the rooms are adjacent, share a doorway, exit off the same corridor, etc.

## Slide 3: Independent work time
Now it’s your turn to draw a bubble diagram!
Follow the instructions on the handout. Complete a bubble diagram using all the required room spaces and all the required spatial relationships listed.
This is due today before the end of class.
Copyright © Texas Education Agency, 2012. All rights reserved.
Notes: Have students use the handout to complete a bubble diagram of their own. The handout lists all the rooms they need to have and some special arrangement requirements that will affect some spatial proximity and layout of the house.

## Slide 4: Pop Quiz
Turn your Handout paper over.
On the back of your handout, answer these 3 questions:
  When is the best time to use a bubble diagram when designing a house? Explain why.
  What do the bubble spaces represent?
  What do the lines between the bubbles represent?
Copyright © Texas Education Agency, 2012. All rights reserved.
Notes: Have students answer these 3 questions on the back side of their handout.

## Slide 5: Pop Quiz – Correct Answers
  The best time to draw a bubble diagram is when you first begin thinking of what the house should look like and where all the rooms should be located.
  The bubble spaces represent rooms/spaces in the house.
  The lines between the bubbles represent connections between rooms/spaces. These lines do not mean there is a hallway, but there could be a door between them or they may be next to each other.
Copyright © Texas Education Agency, 2012. All rights reserved.
Notes: These are the correct answers to the pop quiz questions. Please use this for grading the pop quiz. Phrasing/Wording of student answers should match this wording as closely as possible. This grading uses a 100 point scale. Adjust as needed to meet your grading style. Award them 33 points for every correct answer. If they attempted to answer, but didn’t get it completely right, award them 20 points for each answer. If they didn’t answer the question at all, or if the answer was completely wrong, award them no points at all. Total possible points is 99, with 1 point given as a “bonus” point.